## Slide 1: 1 Ripple Carry Counter
Peter H. Chen

## Slide 2: 1 Ripple Carry Counter
Ripple Carry Counter (0:00/14:22)
We discuss the Ripple Carry Counter.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 3: 1 Ripple Carry Counter
Ripple Carry Counter (0:00/14:22)
Toggle-Flip-Flop.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 4: 1.1 design.v

## Slide 5: 1.1 design.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
Let output is q. It is q flip flop. Should be “reg q” driven.
input are clk and reset.

## Slide 6: 1.1 design.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
An always block is
always @posedge reset because we want to reset the flop.
And we have to clock the flop as well.
We do the reset first,
if (reset) begin,
we drive the output q to zero by non-blocking assignment (<=).
end else
This is the toggle flip-flop
So the basic functionality is the output is going to toggle q <= ~q
So, we close the always block and module here.

## Slide 7: 1.1 design.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
Now, we have to hook up all the flip-flop into a ripple counter.
We call this module ripple_carry_counter.
The inputs the clk and reset.
The output is four bits.
The output here does not need the “reg q”.
We have four toggle flops: ftf0, ttf1, ttf2, tff3.

## Slide 8: 1.1 design.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
Before move on the testbench, we need to make sure there is no compilation error in design.v.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 9: 1.2 testbench.v

## Slide 10: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
The testbench is typically non synthesizable.
So, we can use delays and we can use Verilog initial block here.
Testbench: “module test;”
For testbench, we will use “reg” to hook everything up.
We are going to use clock and reset reg.
The output will be the wire because we are not going to drive it by the testbench.
It is a 4 bits wire. “Wire [3:0] q;”

## Slide 11: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
We are going to instantiate the design here,

## Slide 12: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
We need to dump wave first.
We dump file (“dump.vcd”)
Then, we dump vars.
We dump only 1 level of this test bench.

## Slide 13: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
We set bock to free running.

## Slide 14: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
In order for the clock to be free running, we need to initialize the clock to something.
Here we initialize to zero.

## Slide 15: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
In order to do the test, we are going to reset our ripple carry counter and let it run a little bit.
We reset 1’b1 first
And after sometime (10 tick), we are going to drive reset to 0.
After while (200 ticks), then we are going to reset it again reset = 1’b1;
After 10 tick, we reset to zero again.

## Slide 16: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
Then we run a little bit longer (#50)

## Slide 17: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
We need to finish to prevent it run forever.

## Slide 18: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
Now, we are ready to run.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 19: 1.3 EDA Playground

## Slide 20: 1.3 EDA Playground
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
We can code Verilog model without testbench simulation.
Testbench: Verilog/SystemVerilog
Tools& Simulator: Icarus Verilog 0.9.7
Use Control-s to save design before you run.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 21: 1.3 EDA Playground
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 22: 1.4 Check Result: Incorrect

## Slide 23: 1.4 Check Result: Incorrect
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
Note: Use “x” to close web browser to return.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 24: 1.4 Check Result: Incorrect
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
Why it does not count here? It start with “f”, “e”, “d”, …, 1, 0.
It does not go from “0”, “1”, “2”, …, and etc.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 25: 1.4 Check Result: Incorrect
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
We check the schematics. What ends up happening is because this is the ripple.
When there is a rising edge of the first clock, the output goes to one as we expect.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 26: 1.4 Check Result: Incorrect
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
But the q[0] actually trigger the
next output q[1] as well.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 27: 1.5 Fix 1): negedge Clock

## Slide 28: 1.5 Fix 1): negedge Clock
Fix Counter: negedge lcokc (2:24/14:22)
https://www.edaplayground.com/x/3cf
So, after reset (1’b1), the first clock edge make every (q[3:0]) go to one (?).
If you want to ripple counter to count up 0, 1, 2, 3, 4, 5, …
One way to do, instead of having a trigger on the positive clock edge, trigger on the negative clock edge,
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 29: 1.5 Fix 1): negedge Clock
Run Testbench Again (2:24/14:22)
https://www.edaplayground.com/x/3cf
Now, we have the correct ripple counter: 0, 1, 2, 3, …, a, b, c, d, e, f, and then we reset from 0 again.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 30: 1.6 Fix 2): Invert Output

## Slide 31: 1.6 Fix 2): Invert Output
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
The other way,
we keep the posedge clk
We invert the output ~clk, ~q[0], ~q[1], q[2]
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 32: 1.6 Fix 2): Invert Output
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
Now, we have the correct ripple counter: 0, 1, 2, 3, …, a, b, c, d, e, f, and then we reset from 0 again.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 33: End