## Slide 1: 1 Ripple Carry Counter
Peter H. Chen

## Slide 2: 1 Ripple Carry Counter
Ripple Carry Counter (0:00/14:22)
We discuss the Ripple Carry Counter.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 3: 1 Ripple Carry Counter
Ripple Carry Counter (0:00/14:22)
Toggle-Flip-Flop.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 4: 1 Ripple Carry Counter
Reg and Wire (0:00/14:22)
https://www.researchgate.net/post/Again-what-is-the-difference-between-wire-and-reg-in-Verilog#:~:text=The%20wire%20is%20used%20for,used%20in%20a%20procedural%20assignment.
What is difference between reg and wire? (1)
0reg is a verilog data type that can be synthesized into either sequential or combinational logic depending on how you code it.
Example of a reg that will be synthesized as combinational logic:
reg myreg;
always @ (*) begin
myreg = 1’b0;
End
Example of a reg that will be synthesized as sequential logic (flip flop):
reg myreg;
always @ (posedge clk) begin
myreg <= some_input;
end
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 5: 1 Ripple Carry Counter
Reg and Wire (0:00/14:22)
https://www.researchgate.net/post/Again-what-is-the-difference-between-wire-and-reg-in-Verilog#:~:text=The%20wire%20is%20used%20for,used%20in%20a%20procedural%20assignment.
What is difference between reg and wire? (2)
reg and wire is pretty similar. It depends on how you use it.
Wire is used as combinational logic. You can assign it, e.g. assign a = 1'b1. In this case, the one which holds the value is 1’b1.
Reg can be used as either combinational or sequential logic.
In always@ block, you have to use reg to assign for a value, e.g. '=' or '<=‘.
You cannot use assign with reg.
When reg used in always @(posedge clock), it becomes sequential logic.
The wire is used for a continuous assignment (=) whereas reg is used in a procedural assignment (<=).
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 6: 1 Ripple Carry Counter
Ripple Carry Counter (0:00/14:22)
https://verilogguide.readthedocs.io/en/latest/verilog/procedure.html
What is difference between continuous assignment (=) and procedural assignment (<=)? (1)
Digital design can be broadly categorized in two ways, i.e., combinational designs and sequential designs.
It is very important to understand the differences between these two designs and see the relation between these designs with various elements of Verilog.
Combinational designs : Combinational designs are the designs in which the output of the system depends on present value of the inputs only. Since, the outputs depends on current inputs only, therefore ‘no memory’ is required for these designs. Further, memories are nothing but the ‘flip flops’ in the digital designs, therefore there is no need of ‘flip flops’ in combination designs. In the other words, only ‘logic gates (i.e. and, not and xor etc.)’ are required to implement the combinational designs.
Sequential designs : Sequential designs are the designs in which the output depends on current inputs and previous states of the system. Since output depends on previous states, therefore ‘memories’ are required for these systems. Hence, in the sequential designs the ‘flip flops’ are needed along with the logic gates.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 7: 1 Ripple Carry Counter
Ripple Carry Counter (0:00/14:22)
https://verilogguide.readthedocs.io/en/latest/verilog/procedure.html
What is difference between continuous assignment (=) and procedural assignment (<=)? (2)
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
Fig. Block diagram of ‘combinational’ and ‘sequential’ designs

## Slide 8: 1 Ripple Carry Counter
Ripple Carry Counter (0:00/14:22)
https://verilogguide.readthedocs.io/en/latest/verilog/procedure.html
What is difference between continuous assignment (=) and procedural assignment (<=)? (3)
Blocking and Non-blocking assignment
There are two kinds of assignments which can be used inside the always block, i.e., blocking and non-blocking assignments.
The ‘=’ sign is used in blocking assignment; whereas the ‘<=’ is used for non-blocking assignment.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 9: 1 Ripple Carry Counter
Ripple Carry Counter (0:00/14:22)
https://verilogguide.readthedocs.io/en/latest/verilog/procedure.html
What is difference between continuous assignment (=) and procedural assignment (<=)? (4)
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
// blockAssignment.v
module blockAssignment (
input wire x, y,
output reg z
);
always @(x,y)
begin
z = x; // since z = x
z = z & y; // therefore, z = x + y;
end
endmodule
Fig. Blocking assignment

## Slide 10: 1 Ripple Carry Counter
Ripple Carry Counter (0:00/14:22)
https://verilogguide.readthedocs.io/en/latest/verilog/procedure.html
What is difference between continuous assignment (=) and procedural assignment (<=)? (5)
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
// nonblockAssignment.v
module nonblockAssignment (
input wire x, y,
output reg z
);
always @(x,y)
begin
z <= x; // z_new = x
z <= z & y; // z_new = z_entry + y (not z = z_new + y)
end
endmodule
Fig. Non-blocking assignment

## Slide 11: 1.1 design.v

## Slide 12: 1.1 design.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
Let output is q. It is q flip flop. Should be “reg q” driven.
input are clk and reset.

## Slide 13: 1.1 design.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
An always block is
always @posedge reset because we want to reset the flop.
And we have to clock the flop as well.
We do the reset first,
if (reset) begin,
we drive the output q to zero by non-blocking assignment (<=).
end else
This is the toggle flip-flop
So the basic functionality is the output is going to toggle q <= ~q
So, we close the always block and module here.

## Slide 14: 1.1 design.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
Now, we have to hook up all the flip-flop into a ripple counter.
We call this module ripple_carry_counter.
The inputs the clk and reset.
The output is four bits.
The output here does not need the “reg q”.
We have four toggle flops: ftf0, ttf1, ttf2, tff3.

## Slide 15: 1.1 design.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
Before move on the testbench, we need to make sure there is no compilation error in design.v.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 16: 1.2 testbench.v

## Slide 17: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
The testbench is typically non synthesizable.
So, we can use delays and we can use Verilog initial block here.
Testbench: “module test;”
For testbench, we will use “reg” to hook everything up.
We are going to use clock and reset reg.
The output will be the wire because we are not going to drive it by the testbench.
It is a 4 bits wire. “Wire [3:0] q;”

## Slide 18: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
We are going to instantiate the design here,

## Slide 19: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
We need to dump wave first.
We dump file (“dump.vcd”)
Then, we dump vars.
We dump only 1 level of this test bench.

## Slide 20: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
We set bock to free running.

## Slide 21: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
In order for the clock to be free running, we need to initialize the clock to something.
Here we initialize to zero.

## Slide 22: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
In order to do the test, we are going to reset our ripple carry counter and let it run a little bit.
We reset 1’b1 first
And after sometime (10 tick), we are going to drive reset to 0.
After while (200 ticks), then we are going to reset it again reset = 1’b1;
After 10 tick, we reset to zero again.

## Slide 23: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
Then we run a little bit longer (#50)

## Slide 24: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1
We need to finish to prevent it run forever.

## Slide 25: 1.2 testbench.v
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
Now, we are ready to run.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 26: 1.3 EDA Playground

## Slide 27: 1.3 EDA Playground
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
We can code Verilog model without testbench simulation.
Testbench: Verilog/SystemVerilog
Tools& Simulator: Icarus Verilog 0.9.7
Use Control-s to save design before you run.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 28: 1.3 EDA Playground
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 29: 1.4 Check Result: Incorrect

## Slide 30: 1.4 Check Result: Incorrect
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
Note: Use “x” to close web browser to return.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 31: 1.4 Check Result: Incorrect
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
Why it does not count here? It start with “f”, “e”, “d”, …, 1, 0.
It does not go from “0”, “1”, “2”, …, and etc.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 32: 1.4 Check Result: Incorrect
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
We check the schematics. What ends up happening is because this is the ripple.
When there is a rising edge of the first clock, the output goes to one as we expect.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 33: 1.4 Check Result: Incorrect
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
But the q[0] actually trigger the
next output q[1] as well.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 34: 1.5 Fix 1): negedge Clock

## Slide 35: 1.5 Fix 1): negedge Clock
Fix Counter: negedge lcokc (2:24/14:22)
https://www.edaplayground.com/x/3cf
So, after reset (1’b1), the first clock edge make every (q[3:0]) go to one (?).
If you want to ripple counter to count up 0, 1, 2, 3, 4, 5, …
One way to do, instead of having a trigger on the positive clock edge, trigger on the negative clock edge,
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 36: 1.5 Fix 1): negedge Clock
Run Testbench Again (2:24/14:22)
https://www.edaplayground.com/x/3cf
Now, we have the correct ripple counter: 0, 1, 2, 3, …, a, b, c, d, e, f, and then we reset from 0 again.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 37: 1.6 Fix 2): Invert Output

## Slide 38: 1.6 Fix 2): Invert Output
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
The other way,
we keep the posedge clk
We invert the output ~clk, ~q[0], ~q[1], q[2]
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 39: 1.6 Fix 2): Invert Output
EDA Playground (2:24/14:22)
https://www.edaplayground.com/x/3cf
Now, we have the correct ripple counter: 0, 1, 2, 3, …, a, b, c, d, e, f, and then we reset from 0 again.
https://www.youtube.com/watch?v=eXb8prknDKg&list=PLScWdLzHpkAfbPhzz1NKHDv2clv1SgsMo&index=1

## Slide 40: End